## Slide 1: Chinese ZY-3 Satellite Disclosures: Analysis and Comments, Part 1 Bobby Hunt Amber Iler

## Slide 2: Outline
Purpose
Background
ZY-3 Details
Comments

## Slide 3: Purpose
Fan et al, 2012 1 disclosed optical system details of the Chinese ZY-3 remote sensing satellite
  Described in general terms
  Some elements of optical performance presented with specific details
Careful reading reveals contradictions, ambiguities, and errors
Herein we present our in-depth analysis of Sections I, II, and III(A)
  Basic system requirements/specifications
  MTF results of optical design
  BLUF: Basic optical principles reveal problems with some of the most important aspects of the optical and system capabilities
1 Fan, B., Cai, W., and Hyang Y. “Design and Test of a High Performance Off-axis TMA Telescope” International Conference on Space Optics, 2012

## Slide 4: Summary of Discrepancies
Problem Area | Description | Implication
Unjustified performance values | Optical parameters don’t produce GSD or MTF claimed, and don’t come anywhere near “diffraction limited” | Sensor instability or optical principles flaws may explain discrepancies
Complex optical path | Numerous mirror offsets, no central optical axis, no optical obscurations of other components | May indicate packaging (for launch) problems
Telecentricity without justification | Authors state system is “near telecentric” with no explanation as to why | May not understand value of telecentricity
No common axis | Multiple mirror folds impact optical performance in terms of stability, aberrations, lost photons | Willingness to accept degraded performance over larger system
Rectangular mirror inconsistency | Optical design principles usually avoid geometrically inconsistent reflective surfaces (mixtures of rectangular and circular mirrors) | Manufacturing of mirrors will be unduly complicated
Spectral range questionable | Bandwidth provided is narrower than usual for a multispectral sensor and doesn’t match future systems | Either misstated range or were constrained by unknowns not disclosed in the Paper

## Slide 5: Outline
Purpose
Background
ZY-3 Details
Comments

## Slide 6: Basic Concepts of Optics
Understanding the basics of optical image formation is needed to analyze the ZY-3 information set forth in Fan et al, 2012
Start with a Pinhole Camera
  An enclosed box has a pinhole on one side
  Light rays from all over an object are captured at the pinhole
  Captured light is projected to the opposite end of the box
  These projections form an inverted image of the object
A pinhole camera is very inefficient
  The small aperture allows some light rays to enter, but misses many rays not in the angular range between the object plane, aperture, and image plane
The ZY-3 system wants a sharper, higher contrast image, so it has a more complex optical design compared to a pinhole camera
Aperture (Center of Projection)
Image Plane
Object Plane

## Slide 7: Optics: From Pinhole to Large Aperture
For more contrast and detail, we must gather more light
  Use a larger hole (called the pupil or aperture)
  But a larger hole lets in a wider cone of angles, resulting in blur in the image plane
“Optics” involves lenses or mirrors that reorient light into a tight, pinhole-like focus
  Bending of light is achieved by lens or mirror curvatures in the optical path
Optical surface curvature, and the distance from the pupil/aperture to the image plane (focal length), set the design goals and problems for any optical system
  Fan et al, 2012 summarize these in Sections I, II, and III(A)

## Slide 8: Outline
Purpose
Background
ZY-3 Details
Comments

## Slide 9: Overview of the Optical System of ZY-3
Fan et al, 2012 states the satellite optics design is a Three Mirror Anastigmat (TMA)
A TMA optical design minimizes optical aberrations:
  Spherical aberrations
    Rays at the center vs. edge of the entrance aperture pupil do not focus at the same distance
  Coma aberrations
    Small point objects, away from the optical central axis, develop tails (like a comet…) in the image
  Astigmatism aberrations
    Details in a horizontal direction focus into a different distance than those in a vertical direction
  A three-mirror design gives more flexibility to correct aberrations
An on-axis design is easier to align optically to the wavelength level
The ZY-3 optical design (called the “Optical Demonstration Model” – ODM) is very different from a pinhole camera or common on-axis telescope designs!
  There are mirror offsets, no central optical axis, no optical obscurations of other components
  This design does enable a wider field-of-view (FOV)
On-Axis TMA Design
Primary
Secondary
Tertiary
Image Plane

## Slide 10: Optical System Design Details of ZY-3
The TMA ODM optical elements are specified as:
  The overall focal length stated as f = 1.75 m
  An optically flat fold mirror makes the imaging design compact: see the optical layout below
    Suggests “packaging” limitations, probably imposed by aerodynamics of the orbital booster
The paper states the “The optical system is nearly a telecentric system.”
  Telecentric designs place an aperture stop in the optical path at a point where principal rays are parallel
  Design shows rays from the concave primary nearly parallel
  Convex secondary projects parallel rays to the tertiary mirror
  The paper directly states the secondary is an aperture stop, confirming near telecentricity
Mirror | Surface Shape | Dimensions (mm)
Primary (concave) | 2nd order Hyperboloid | 316 x 217
Secondary (convex) | 2nd order Hyperboloid | Diameter 102 (Circular)
Tertiary (convex) | 2nd order Ellipsoid | 250 x 150
Fold mirror | Flat | 217 x 91

## Slide 11: “Nearly” Telecentric Optics in ZY-3
Parallel rays are significant in image formation
  Parallel rays propagate from very remote objects
  Rays of objects in 3-space converge toward the focal point of optics
  Optical curvature alters convergence and make rays parallel for an angular range
  An aperture stop at the proper point passes only the parallel rays
Visualize in the context of “Vanishing Point”
  Ordinary, non-telecentric optics make distant objects smaller in the focal plane
  Telecentricity means objects at different distances do not change size in the focal plane image – the vanishing point effect is greatly reduced or eliminated
  Important for an optical system with a wide FOV
    Objects at extremes away from the center point will not appear different in size
The ZY-3 optical design adopts this for line-scan FOV imagery
  The FOV is 6 x 1 , suited for line-scan push-broom imaging operations
  By being “nearly” telecentric, the need for correction of push-broom image details away from center is minimal
Ordinary
Optics*
Telecentric
Optics*
*https://evidentscientific.com/en/insights/telecentric-optics-101-all-the-basics-you-need-to-know

## Slide 12: Gleaning Information from the “Optical System Design Details of ZY-3”
The layout shows the design to have no common axis
  Common axis = Shared central alignment of optical components
  Lack of common axis is atypical in telescope designs with multiple mirrors due to manufacture, alignment, and stability complexity
  Benefit: ODM has no optical obscuration that blocks photons
The Primary, Tertiary , and Fold mirrors are rectangular
  This is unusual, but is consistent with a stated pushbroom sensor architecture due to elongated focal plane array
  The small Secondary mirror is circular in shape
    Confirmed from a less-known convention to designate a diameter with the Greek symbol
  Greater length rectangular mirror dimensions must be “into the page” of the diagram above
    The apparent sizes are only consistent if the short rectangle edges are displayed
  The small Secondary promotes the “nearly” telecentric design
    Telecentricity requires an aperture stop
    A larger secondary would have allowed rays of greater divergence from parallel, defeating telecentric functioning

## Slide 13: ZY-3 01 vs. ZY-3 03 Sensor Comparisons
Section II of the paper alludes to “market demand”
  This implies possible commercial sale of satellite mapping products
  China’s first high resolution, stereoscopic mapping satellite for civilian use
The current ZY-3 satellite (ZY-3 03, launched in 2021) improved over specifications in Fan et al, 2012
  GSD of stereo Pan improved
    Gyro sampling frequency improved from 4 Hz to 8 Hz
    Optical diffraction-limited GSD improved from 2.7 m to 2.6 m
    Structural stability upgrades
    Pixel pitch remained unchanged
  Spectral range specified as wider
    Fan et al, 2012 range more likely specific to Pan, not MSI
  Now includes a laser altimeter
Sensor Characteristic | ZY-3 01 (Fan et al, 2012) | ZY-3 03
Nadir Pan GSD | 2.1 m | 2.1 m
Forward/Backward Stereo Pan GSD | 3.5 m | 2.6 m
Pan Pixel Pitch (microns) | 7 | 7
Multispectral (4-band VNIR) GSD | 5.8 m | 5.8 m
Spectral Range (microns) | 0.5-0.8 | 0.45-0.89
Laser Altimeter (1 m elev. accuracy) | X | ✓

## Slide 14: MTF Statements in Fan et al, 2012
Fan et al, 2012 asserts:
  “nearly diffraction limited performance” (under Table II)
  MTF 0.456 for all MTF values
Modulation Transfer Function (MTF) is the magnitude of the Optical Transfer Function (OTF) of any optical device, based on the physics of diffraction
  MTF tells you the diffraction limited resolution of the optics as a function of spatial frequency
  At right below are MTFs for circular optics with varying circular obscurations (black)
  A simple line from zero to cutoff spatial frequency at 1.0 is expected in Fan et al, 2012
    i.e., no obscurations
  MTF 0.456 is not meaningful in the absence of obscurations, because diffraction limited MTFs are zero cutoff spatial frequency
  This is also true for rectangular optics
In the following, we examine the contradictions in these statements, from physical optics

## Slide 15: Sampling of Optical Data
Digital sampling impacts spatial frequency information
  As seen on the previous slide, the optical MTF must go to zero
  The point where MTF goes to zero is known as the “diffraction-limited cut-off”
  What does this mean when Fan et al, 2012 states: MTF 0.456 for all MTF values
The physics of diffraction, combined with the mathematics of sampled data, mean that the ODM of ZY-3 cannot give “nearly diffraction limited performance”
  The images collected by ZY-3 optics are recorded by a digital focal plane
    The focal plane samples the optical field over small areas – the 7 m focal plane detector pixels
Diffraction limited performance is contraindicated because:
  Diffraction physics forces any optical MTF to zero beyond some value of spatial frequency
  The spatial frequency where the MTF goes to zero imposes a critical size for sampling pixels
    If the sampling pixels are greater than the critical size the result is to distort the optical information collected in the samples
    This distortion is called “aliasing” of data or information
The next slide illustrates actual effects of aliasing

## Slide 16: Example of Optical Aliasing Effects (1 of 2)
Original
Aliased

## Slide 17: Example of Optical Aliasing Effects (2 of 2)
The previous slide shows two examples of a classic 1950’s TV Test Pattern
  The left image is the original test pattern
  The right image shows the effects of aliasing, as created when the image is sampled with pixels that are twice as large as allowed by the actual resolution of the optical system
There are three “classic” distortions present in this image
  (1) Notice that the general background is “whiter” in the image on the right
    This is because of the added energy that is present by collecting samples with more light energy than the smaller pixels for the diffraction limit of the optics
  (2) Notice how smooth lines in the left image have become “jagged” or “stair-stepped”
    This is sometimes referred to as “pixelation” of features
  (3) Notice how adjacent lines in the converging horizonal / vertical patterns merge or disappear
    This is due to features being clumped together by the improper sample size

## Slide 18: Quality Factor (Q) Metric
Image science specifies diffraction limited sampling sampling by the Quality factor, Q
Pixel pitch (spacing) relates to sensor Q as:
  To accurately reconstruct a signal, pixels must sample at least twice the highest spatial present
    Q = 2 (Nyquist sampling) for samples without aliasing
    The upper graphic at right shows this in spatial frequency
When Q < 2, aliasing is the result
  This occurs when optics can resolve spatial features, but detectors are too wide to sense separations in the optical field falling on the detector pixels
  The lower graphic at right shows how sampling in the focal plane creates spatial domain aliasing
  The Test Pattern previous emphasizes frequency domain effects of aliasing
Fiete, 1999. Opt. Eng. 38(7), 1229-1240.

## Slide 19: Conclusions to Draw from MTF Data presented in Fan et al 2012 (1 of 2)
The method by which MTF was measured is not explicitly stated
  The logical assumption is that focal plane data was used with some kind of test chart
MTF 0.456, demonstrates that the data was undersampled
  Data values added together at larger sample spacing cause a lower limit to the MTF as in plot on the top of the previous slide
  This can be seen from sampling calculations for ZY-3 using the “Quality Factor”, :
  Where, = the illumination wavelength, = optical F-Number, = detector sample size (“pitch”)
    For ZY-3, with = 550 nm, = 1.75/0.217 (primary smallest dimension), = 7 , we have:
    And for the case of the largest primary dimension (0.316 m)
    Unfortunately, to prevent subsampling errors: the required value is

## Slide 20: Conclusions to Draw from MTF Data presented in Fan et al 2012 (2 of 2)
The focal plane sampling present in the ZY-3 optical system is the reason that measured MTF values were
  A test chart for MTF measurements will have a given spectral content, and a good test chart will contain sufficient detail for very high spatial frequency content
    The test chart spatial frequency spectrum will go to zero at the optical diffraction limit cutoff
  In the optical system for the ZY-3 ODM, overlapping of optical information, as indicated by Q, add to no MTF values less than
  For the 7 detector pixels the optical focal length must be increased, the primary aperture sizes decreased, or some combination of the two, to prevent subsampling errors
For “nearly diffraction limited performance”, MTF values approach at the maximum resolvable spatial frequency
  Fan et al, 2012 does not explain the reason for MTF values being limited to a “floor value” of
  It is unclear if the authors are aware of the sampling problems and effects being described here

## Slide 21: Pixel Size and GSD
Fan et al, 2012 states panchromatic 7 um pixel pitch
  Cell phone cameras can have pixels that are much smaller (1-3 um)
  7 um pixel size is common for science sensors (for astronomy or high spatial resolution)
  State-of-the-art TDI sensors are often this size
    Teledyne offers high-speed, high-resolution CMOS TDI sensors at 7 um
    Typical range is 3.5-7 um
Stated 7 um pitch does not equate to 3.5 m GSD at 500 km altitude:
Thus:
  Discrepancy may be due to stability issues, imprecise absolute altitude, discussed sampling error
    Both significantly improved on ZY-3 03, enabling near diffraction-limited performance

## Slide 22: What Does Choice of Spectral Range Tell Us?
Spectral range of 500-800 nm indicates:
  Sensitivity in visible band from green through near-infrared (NIR)
    Typical of silicon-based sensors
    Blue light typically 400-500 nm
    Standard NIR wavelengths used for night vision/CCTV: 850 and 940 nm
Reasons for blue exclusion
  Rayleigh (atmospheric) scattering causes haze and noise for blue photons
  Most CCD and CMOS sensors are less efficient in the blue band, resulting in higher noise
  Assumes no need for water penetration
We suspect range provided refers to Pan band and multispectral range may extend further with specialized calibration of blue and NIR bands
Courtesy: Teledyne Princeton Instruments

## Slide 23: Outline
Purpose
Background
ZY-3 Details
Comments

## Slide 24: Summary of Findings
Problem Area | Description | Implication
Unjustified performance values | Optical parameters don’t produce GSD or MTF claimed, and don’t come anywhere near “diffraction limited” | Sensor instability or optical principles flaws may explain discrepancies
Complex optical path | Numerous mirror offsets, no central optical axis, no optical obscurations of other components | May indicate packaging (for launch) problems
Telecentricity without justification | Authors state system is “near telecentric” with no explanation as to why | May not understand value of telecentricity
No common axis | Multiple mirror folds impact optical performance in terms of stability, aberrations, lost photons | Willingness to accept degraded performance over larger system
Rectangular mirror inconsistency | Optical design principles usually avoid geometrically inconsistent reflective surfaces (mixtures of rectangular and circular mirrors) | Manufacturing of mirrors will be unduly complicated
Spectral range questionable | Bandwidth provided is narrower than usual for a multispectral sensor and doesn’t match future systems | Either misstated range or were constrained by unknowns not disclosed in the Paper

## Slide 25: Comments on the Optical Disclosures in Fan et al, 2012 (1 of 4)
Choice of pixel pitch had consequences to GSD and MTF
  A smaller pitch would have improved GSD
  Smaller pitch would have minimized distortions due to aliasing and improved the MTF
  Could the choice of pixel size been a consequence of high performance semiconductor trade restrictions?
Fan et al, 2012 paper is unclear about whether additional optical paths exist
  Both stereo Pan and multispectral referred to, but specifications only refer to ODM
  Stereo Pan GSD substantially worse than Forward/Backward Stereo Pan GSD on ZY-3 03
    Sensor instability or optical principles flaws may explain discrepancies
  Implies multiple cameras that are not described in the context of ODM as a “Model” for systems
The overall optical design features, in pursuit of “high resolution stereo mapping”, are significant for building competence in space system optics
  Hyperboloid optical designs offer the elimination of the off-axis coma aberrations, and are an important improvement to the classical Cassegrain telescope
  Advances in optical metrology, during figuring and polishing mirrors, have made more complex designs a cost-feasible capability for optical telescopes
  Three-mirror anastigmats are sophisticated optical designs
    James Webb Space telescope is a TMA design

## Slide 26: Comments on the Optical Disclosures in Fan et al, 2012 (2 of 4)
The advantages of “nearly” telecentric TMA design, and the extra complexity of same, also support the design goals of “high-resolution stereo mapping”
  Minimal distortions in raw image data yield a minimum of optical distortion computations in the compilation of precision mapping products
Summarizing Fan et al, the two main optical “design themes” are:
  TMA optics
  Telecentric optics
When these two themes are considered together, they support the desire for a “high-resolution stereo-mapping” optical system
  TMA designs minimize distortions of objects within the optical field-of-view, due to the inherent limitations of simpler optical designs
  Telecentric designs minimize distortions due to different distances from the focal plane to objects within in the optical field-of-view
  Images, and products from images, with these characteristics are simpler and less-costly to produce, meeting goals that can be associated with “market demand”

## Slide 27: Comments on the Optical Disclosures in Fan et al, 2012 (3 of 4)
Since “market demand” is not often a goal of Chinese state-funded projects, an additional question occurs:
  What other capabilities are enabled by the experience to build a “high-resolution stereo mapping” optical system? For example: strategic/tactical reconnaissance?
It is worth noting that Fan et al, 2012 explicitly states that the elements in the optical design come from a desire to create an “Optical Demonstration Model” (ODM)
  The acronym “ODM” occurs six times in the opening paragraphs of the paper
This focus suggests a strong desire in the optical design team to:
  Work through various elements of optical design for ZY-3 sensors
  Understand the pros/cons of different optical trade-offs
  Gain experience in actual construction and packaging of sensors prior to commitment into a launch-qualified system
  Create a legacy that would survive to guide subsequent modifications and upgrades for improved and advanced versions
  Build capability and credibility for Chinese Government optical capabilities and applications
Total “spectral range” is substandard to state-of-the-art multispectral systems
  No blue for water, and shortened IR limits use for many survey applications
  The stated range is more common for Pan cameras

## Slide 28: Comments on the Optical Disclosures in Fan et al, 2012 (4 of 4)
It is worth noting that Fan et al, 2012 explicitly states that the elements in the optical design come from a desire to create an “Optical Demonstration Model” (ODM)
  The acronym “ODM” occurs six times in the opening paragraphs of the paper
This focus suggests a strong desire in the optical design team to:
  Work through various elements of optical design for ZY-3 sensors
  Understand the pros/cons of different optical trade-offs
  Gain experience in actual construction and packaging of sensors prior to commitment into a launch-qualified system
  Create a legacy that would survive to guide subsequent modifications and upgrades for improved and advanced versions
  Build capability and credibility for Chinese Government optical capabilities and applications

## Slide 29: Concerns for the Information Disclosed in Fan et al, 2012
The comments above are offered to be a background of motivations and design framework for interpreting the information disclosed
However, there are “contradictions, ambiguities, and errors” in the actual details that are disclosed
It is also possible the difficulties with Fan et al, 2012 content are known to responsible individuals in China, and the paper is considered more as publicity than archival
In this spirit, we have identified problems with blindly or unconditionally accepting the material in Fan et al, 2012

## Slide 30: Thank you.